## Slide 1
SP-3000-148
DC48V → AC100V 3000W Inverter Detailed System Block Diagram

## Slide 2
Overall System Block Diagram
Front panel board DIP-SW / LED/TRC port (RJ-45) / P-Sav adjustment
CN3(16P)
Upper Power Board DC/DC Step-Up / High-Frequency Transformer H-Bridge PWM / LC Filter
DC48V input
AC100V Output
Busbar connection
Rear panel board Remote port (RJ-11) / RC port
Lower power board DC/DC Step-Up / High-Frequency Transformer H-Bridge PWM / LC Filter
CN2 (8P) communication
front panel Power Supply - SW
(3P)
Busbar connection
(3P)
Upper Control Board 66-BA97-2101 MCU / DIP=010 / Buzzer
Lower control board 66-BA97-2101 MCU / DIP=001 / Buzzer

## Slide 3
Control Configuration and Communication Flow
[Upper System]
Upper Control Board (Master) MCU DIP=010
Upper Power Board PWM Control Boost and Reverse Conversion
CN2(8P)通信
・Synchronization signals ・Current sharing ・Abnormal notifications
[Lower Tier System]
Lower control board (Slave) MCU DIP=001
Lower power board PWM Control Boost and Reverse Conversion
■ Control Flow Details
1. Power Control: Simultaneous ON/OFF of power to upper and lower levels via the front panel power SW 2. Input Power Distribution: DC48V input is distributed between upper and lower stages, with independent voltage boost and reverse conversion performed at each stage. 3. Synchronization control: The CN2 communication line synchronizes the upper stage (master) with the lower stage (slave) - PWM frequency and phase synchronization - Equal distribution of output current (parallel operation) - Simultaneous shutdown upon anomaly detection 4. Output synthesis: Parallel AC100V output in two stages to supply up to 3000W of power 5. Protection function: Buzzer alerts abnormalities in cases of overcurrent, overtemperature, or low input voltage

## Slide 4
Power flow configuration
[Top Level: Power Flow]
DC48V input
DC/DC Boost
High frequency Trans
H-Bridge PWM
LC filter
AC100V Output Up to 1500W
[Bottom Section: Power Flow]
DC48V input
DC/DC Boost
High frequency Trans
H-Bridge PWM
LC filter
AC100V Output Up to 1500W
【出力並列合成】
AC parallel connection Up to 3000W
■ Power Processing Steps
1. DC/DC Boost: Boost the input DC 48V to generate DC voltage for H-bridge drive (efficiency: ~95%) 2. High-frequency transformer: Converts step-up DC voltage with an isolated transformer (miniaturization at high frequency) 3. H-Bridge Inverse Conversion: DC → AC inverse conversion using MCU's PWM control signal (frequency: selectable 50/60Hz) 4. LC filter: Removes the switching frequency of PWM to generate pure sine wave AC100V output 5. Parallel power: Parallel output of 3000W by paralleling the upper and lower stages (load balancing)

## Slide 5
Interface Specifications
■ CN3 (16P) - Front panel
Application: Connection to the front panel Signal Composition: ・Power supply switch (input) ・LED display signal (output) ・Buzzer control (output) ・Status signal (output) Connector: 16-pin DIN type
■ CN2 (8P) - Inter-control board communication
Purpose: Communication between upper and lower MCUs Communication content: ・PWM synchronization signal ・Output current information ・Abnormal notification ・Slave control Connector: 8-pin DIN type
■ External Remote Connector
Application: External control input Features: ・Remote power control ・Status monitoring (output available) ・Abnormal signal output Via the rear panel board Control Board and Connection
■ Control Board Specifications (66-BA97-2101)
[Upper Control Board] DIP setting: 0 1 0 (Master, Sync Trigger, Normal Mode) Features: ・Front panel system ・PWM waveform generation ・Current detection & feedback ・Abnormality detection & notification ・Buzzer control
[Lower Control Board] DIP setting: 0 0 1 (Slave, sync reception, normal mode) Features: ・Synchronized reception with the upper platform ・PWM waveform generation (synchronization) ・Current detection & feedback ・Abnormality detection & notification

## Slide 6
System Specifications
■ Input/Output Specifications
[Input] ・Voltage: DC48V ±10% ・Maximum input current: 65A each for the upper and lower stages (total 130A) ・Maximum input power: 6240W (DC48V×130A) [Output] ・Voltage: AC100V ±5% ・Frequency: 50/60Hz (optional) ・Maximum output power: 3000W (total of upper and lower sections 1500W×2) ・Waveform: Pure sine wave (THD≦3%)
■ Performance
■ Conversion efficiency: ≧92% (estimated) ・DC/DC Step-Up Step: ~95% ・H-Bridge Inverse Conversion: ~97% ・Transformer & filter loss: ~98% ■ Response Speed ・Startup time: <500ms ・Sync lock time: <100ms ・Anomaly detection: Real-time ■ Cooling: Forced air cooling or natural convection
■ Operating Specifications
■ System Requirements ・Temperature range: -10°C~+50°C (recommended 0~40°C) ・Humidity range: 20~80% (no condensation) ・Altitude: <2000m ■ Protection Features ・Overcurrent protection: Implemented on all output lines (automatic shutdown) ・Overtemperature protection: monitored by temperature sensor (warning → shutdown) ・Low input voltage protection: Cutoff at DC48V<43.2V ・Synchronization error protection: automatically turns off the lower stage when CN2 communication is interrupted. ・Abnormality notifications: Instant display with buzzer and LED display ■ Insulation Withstand Voltage ・Between input~output: DC3000V, 1 minute (compliant with safety standards) ・Inter-signal circuit: DC500V, 1 minute